## Slide 1: Respiratory Protection
User Training – Pest Control
Presented by:
Notes: 1
Revised 2/2022
The information in this presentation is provided voluntarily by PestSure Safety and loss prevention as a service and is made available in good faith. This presentation is designed to assist trainers conducting respirator training for pest control technicians. Since workers are the target audience, this presentation emphasizes hazard identification, avoidance, and control – not standards. No attempt has been made to treat the topic exhaustively. It is essential that trainers tailor their presentations to the needs and understanding of their audience.
TRAINER: OBTAIN THESE HANDOUTS FOR USE IN THIS CLASS:
Appendix A to § 1910.134: Fit Testing Procedures
Appendix B-1 to § 1910.134: User Seal Check Procedures
Appendix B-2 to § 1910.134: Respirator Cleaning Procedures
Appendix C to § 1910.134: OSHA Respirator Medical Evaluation Questionnaire
Appendix D to § 1910.134: Information for Employees Using Respirators When Not Required Under the Standard

## Slide 2: Objectives
1910.134
At the end of this course, students should be aware of :
  Potential respiratory hazards in your workplace
  Respirator type/use and limitations
  Identifying medical signs and symptoms that limit use
Hands on Practice:
  Putting on your respirator and properly adjusting it
  Conducting your user seal check
  How we use, maintain, store and care for our respirators

## Slide 3: Part 1
Our Respiratory Safety Program Administrator is:
1910.134(c)

## Slide 4: Part 2
Medical Evaluation
1910.134(e)

## Slide 5: Why Have Medical Evaluations?
1910.134(e)
A respirator places a physiological burden on the user.
This burden varies with:
  Type of respirator worn.
  Job and workplace conditions.
  Medical status of the employee.
You will have a medical evaluation prior to fit testing.

## Slide 6: Physiological Effects
Pulmonary
Cardiovascular
Body temperature
Senses
Psychological
Irritation and allergy

## Slide 7: Medical Evaluation
Establishes the medical condition of the wearer.
Provided before initial respirator use.
Prior to fit testing and training.
Performed by a physician or other licensed health care professional (PLHCP).
1910.134(e)

## Slide 8: Part 3
Selection
1910.134(d)

## Slide 9: Hazard Determination
Identify the contaminants and evaluate the hazards.
Determine the physical properties of the contaminants.
Identify areas of potential oxygen (O2) deficiency.
Estimate or measure employee’s exposure to the hazards.
1910.134(d)

## Slide 10
Oxygen-deficient atmosphere
  Does not contain enough oxygen to sustain breathing. (<19.5 percent by volume at sea level).
    Examples:
      Confined spaces
      Silos
      Boilers
      Tanks
      Sewers
Immediately dangerous to life or health (IDLH) or unknown atmosphere.
Hazards Requiring Respirator Use

## Slide 11
Chemical hazards
  Overexposure to workplace contaminants such as: dust, spray, fumes, vapors, smoke, harmful gases.
Biological hazards
  Exposure to organisms such as bacteria, viruses, fungi and other living organisms. (These organisms do not have exposure limits.)
Hazards Requiring Respirator Use
NCDOL Photo Library
NCDOL Photo Library

## Slide 12: Hierarchy of Controls
1910.134(d)
Engineering controls
  Example:
    Ventilation
Administrative/work practice controls
  Examples:
    Rotating employees to reduce exposure time.
    Limiting the time someone can work in an area.
    Changing the way the work process is conducted.
Personal protective equipment (PPE)
  Used when unable to eliminate or reduce the hazard sufficiently.

## Slide 13: What is a Respirator?
A device that protects workers by purifying air or by providing an air supply (O2 deficiency or IDLH conditions).
Two main types of respirator:
  Air-purifying respirators remove contaminants from breathing air through a filter, cartridge or canister.
  Supplied-air respirators provide clean air from an uncontaminated source such as bottle or compressor.

## Slide 14: Selection
Select the appropriate respirator based on the hazard, workplace and user factors.
Select only NIOSH-certified respirators.
Provide sufficient number of respirator models and sizes to correctly fit user.
1910.134(d)(1)
NCDOL Photo Library
NCDOL Photo Library
Notes: .

## Slide 15: The SDS: information in Section 8

## Slide 16: Air-Purifying Respirators (APR)
1910.134
Filtering
Facepiece
Full Facepiece Respirator
(with Organic Vapor Cartridges)
Half Mask Respirator
(with Combination Cartridges)
NCDOL Photo Library
NCDOL Photo Library
NCDOL Photo Library

## Slide 17: Filtering Facepiece (Dust Mask)
1910.134
NCDOL Photo Library
Negative pressure particulate respirator
with entire or majority of face piece
composed of a filtering medium..
Captures particles in the air, such as
dusts, aerosols, mists, and fumes.
Filters will be labeled with a letter N, R or P
and a number representing the efficiency: 95, 99 or 100.
Does not protect against gases or vapors.
Replace filters when the user finds it difficult to breathe.

## Slide 18: Respirators with Combination Cartridges
Full Facepiece and Half Mask
  Used in atmospheres that contain both
  particulates and gases or vapors.
  Have both particulate filters and gas/vapor
  cartridges or canisters.
  Not for use in oxygen-deficient atmospheres or atmospheres which have high concentrations of contaminants (such as IDLH).
  Breathing may become difficult because of the additional effort required to draw air through the purifying medium.
1910.134
NCDOL Photo Library

## Slide 19: Respirators with Organic Vapor Cartridges
Full Facepiece and Half Mask
  Does not protect against airborne particles.
  Provides protection only as long as the filter’s absorbing capacity is not depleted.
  Uses chemical filters (called cartridges or canisters) to remove specific dangerous gases or vapors.
  Service life of the filter depends upon
  many factors and can be estimated in
  various ways.
1910.134
NCDOL Photo Library

## Slide 20: Cartridge/Canister Service Life
Conditions affecting service life:
  Exertion level
  Cartridge variability
  Temperature
  Humidity
  Multiple contaminants
1910.134(j)

## Slide 21: Filters/Cartridges/Canister Labels
Only NIOSH approved.
Labeled and color coded.
Label shall not be removed and remains legible.
1910.134(j)
NCDOL Photo Library

## Slide 22: Part 4 Training and Information

## Slide 23: Training and Information
1910.134(k)(1)
Why the respirator is necessary and how improper fit, usage, or maintenance can compromise the protective effect of the respirator.
Limitations and capabilities of the respirator.
How to effectively use the respirator in emergencies.

## Slide 24: Training and Information
1910.134(k)(1)
How to inspect, don, doff, use, perform seal checks.
Maintenance and storage procedures.
How to recognize medical signs and symptoms that may limit or prevent the effective use of respirator.
https://youtu.be/LII-z2WJ4Dc

## Slide 25: Part 5 Fit Testing
1910.134(f)

## Slide 26: When is Fit Testing Required?
Before initial use
Annually, thereafter
When facial features change, such as with weight gain or loss, use of dentures
Note: Employees wearing tight-fitting face-pieces
must not be fit tested if they have facial hair *
1910.134(f)

## Slide 27: Qualitative Fit Test (QLFT)
A pass/fail fit test to assess the adequacy of respirator fit that relies on the individual’s response to the test agent.
Must not be used if a person has no sense of taste or smell.
Used for respirators requiring a fit factor of 100 or less.
1910.134(f)

## Slide 28: Part 6 Maintenance and Care
1910.134(h)

## Slide 29: Cleaning and Disinfecting
Respirators must be clean, sanitary, and in good working order.
Respirators must be cleaned and disinfected using the procedures on the next 2 slides or procedures recommended by the respirator manufacturer.
1910.134(h)(1)

## Slide 30: Respirator Cleaning

## Slide 31: Respirator Cleaning - continued
https://youtu.be/ScvkveNQqMc

## Slide 32: Cleaning and Disinfecting
Respirators cleaned and disinfected at the following intervals:
  If exclusive use by employee – as often as necessary to be maintained in a sanitary condition.
  If shared by employees – prior to each use by different employee.
  If for emergency use – after each use.
  If used for training and fit testing – between each employee and at the end of each training/fit testing session.
1910.134(h)(1)

## Slide 33: Storage
Respirators must be protected from:
  Dust
  Sunlight
  Heat
  Cold
  Moisture
  Chemicals
  Stored in a sealed container or bag
1910.134(h)(2)
Notes: .

## Slide 34: Inspection
Check for:
  Holes in the filters
  Loss of elasticity or tears in the head straps and hoses
  Broken or loose connectors and fittings
  Cracked or scratched face pieces
  Detergent residue
  Dirt in the valves
  General cleanliness
1910.134(h)(3)

## Slide 35: Repairs
Respirators that fail an inspection or are otherwise found to be defective are removed from service and discarded or repaired/adjusted.
  Repairs made only by appropriately trained persons.
  Use only respirator manufacturer’s NIOSH-approved parts.
1910.134(h)(4)
Notes: .

## Slide 36: Part 7
Use
1910.134(g)
Notes: .

## Slide 37: Use of Respirators
Always put respirator on in clean air environment.
Always seal-check the respirator to make sure proper fit has been achieved for tight-fitting respirators.
Two types of user seal checks (demonstrate):
1910.134(g)
NCDOL photo library
NCDOL photo library
Negative Pressure
Positive Pressure

## Slide 38: Use
Respirators are only effective when the seal around your nose and mouth is tight.
  If you cannot achieve proper fit, do not enter the contaminated area.
Facial hair cannot inhibit the seal when wearing a tight-fitting respirator.
Glasses cannot be worn with
a full-face respirator.
  Spectacle kit required
1910.134(g)(1)
NCDOL photo library

## Slide 39: Use
Leave the contaminated atmosphere if any of the following occurs:
  Smell or taste something out of the ordinary
  Eyes or throat become irritated
  Observe a change in breathing
  Face piece is leaking or other parts break
1910.134(g)(2)

## Slide 40: Part 10
Voluntary Use
1910.134(c)
Notes: 1910.134(o) and 1910.134 Appendix D

## Slide 41: Voluntary Use
1910.134(c)(2)
NCDOL Photo Library
NCDOL Photo Library
For all respirators, the employer must:
  Determine that voluntary use is appropriate.
  Ensure that use of the selected respirator will not create a hazard.
  Provide employees with information in Appendix D.
For all respirators except filtering face pieces, the employer will address:
  Medical evaluations, and
  Training on maintenance, storage and care.

## Slide 42: Handouts Trainer – obtain from program administrator for use in this class
Appendix A to § 1910.134: Fit Testing Procedures
Appendix B-1 to § 1910.134: User Seal Check Procedures
Appendix B-2 to § 1910.134: Respirator Cleaning Procedures
Appendix C to § 1910.134: OSHA Respirator Medical Evaluation Questionnaire
Appendix D to § 1910.134: Information for Employees Using Respirators When Not Required Under the Standard
1910.134

## Slide 43: Objectives
1910.134
At the end of this course, students should be aware of :
  Potential respiratory hazards in your workplace
  Respirator type/use and limitations
  Identifying medical signs and symptoms that limit use
Hands on Practice
  Putting on your respirator and properly adjusting it
  Conducting your user seal check
  How we use, maintain, store and care for our respirators

## Slide 44: Please ask any questions.
Discussion?
Notes: 44